## Slide 1: Data communication ENG Mosa ELkhedr

## Slide 2
Course Introduction

## Slide 3: Networking Technologies
Network:
is basically all the components (H/W &
S/W) involved in connecting computer across
small and large distance
Importance of Networks:
  Easy access and sharing of information
  Sharing of expensive devices and network
  resources
  Modern Technologies (IP telephony, Video
  on Demand, ….etc)

## Slide 4: Network components
Network has three main components
  Computers (servers and hosts)
  - Source of applications (network aware applications)
  - ex: HTTP (Hyper Text Transmission Protocol),
  FTP (File Transfer Protocol),
  SNMP (Simple Network Management Protocol)
  Telnet
  Network Devices
  - Devices that interconnect different computers together
  - ex: Repeaters, hub, bridge, switch, router, NIC and modems
  Connectivity
  - Media that physically connect the computers and network devices
  - ex: Wireless and cables

## Slide 5: Network Types
LAN (Local Area Network):
It is a group of network components that work
within small area
WAN (Wide Area Network):
It is a group of LANs that are interconnected
within large area

## Slide 6: Reference Models
- describe data transfer standards
- a framework (guideline) for network implementation and troubleshooting
- Reference model types :
- OSI
- TCP/IP

## Slide 7: Reference Models
7 Application
6 Presentation
5 Session
4 Transport
3 Network
2 Data Link
1 Physical
Application
Transport
Internet
Network Access
The TCP/IP Model
The OSI Model

## Slide 8: Hierarchical Network Model

## Slide 9
9
The Physical Layer
Notes: Purpose: This chapter introduces the Cisco IOS™ CLI on the Catalyst® 1900 switch and router.
Timing: This chapter should take about 2 hours to present.
Note: The Catalyst 1900 switch only has a subset of the router Cisco IOS commands available.
Contents:
  Introduction to Cisco IOS. Explain to the student what is IOS?
  Cisco Device startup procedures in general.
  IOS configuration source.
  General introduction to the IOS CLI.
  Cat 1900 switch startup procedures.
  Intro to Cat 1900 CLI. This part covers the basic configuration on the switch, like setting the IP address and hostname. More details about the various Cat 1900 switch configuration commands are explained in Chapter 6 and 7.
  Router startup procedures. More details on the router startup process is discussed in chapter 5.
  Router IOS CLI.

## Slide 10: Physical Layer Responsibilities
Description of LAN/WAN cables & connectors
Description of LAN/WAN standards
(maximum length, bit rates, pin assignment, voltage levels)
Physical Layer Devices

## Slide 11: LAN Physical Layer
Ethernet cables :
- Copper ( UTP , STP , Coaxial )
- Fiber

## Slide 12: Unshielded Twisted Pair (UTP) Cable
CAT5
CAT 5e , CAT6
RJ-45
prevents EMI , RFI
to avoid attenuation

## Slide 13: Using UTP cable to connect devices
1- straight cable
2- cross cable
3- roll over cable

## Slide 14: Straight-Through or Crossover cables
PC
router
switch
hub
modem
Cross cable
straight cable
Cross cable

## Slide 15: Straight Cable
Straight or cross
Straight Cable
Usually use straight cable to connect different type of devices. This type of cable will be used most of the time and can be used to:
1) Connect a computer to a switch/hub's normal port.
2) Connect a computer to a cable/DSL modem's LAN port.
Crossover Cable
Sometimes you will use crossover cable, it's usually used to connect same type of devices. A crossover cable can be used to:
1) Connect two computers directly.
2) Connect a router's LAN port to a switch/hub's normal port. (Normally used for expanding network)
3) Connect two switches/hubs by using normal port in both switches/hubs.

## Slide 16: Shielded Twisted Pair (STP) Cable

## Slide 17: Coaxial Cable
thick coaxial , thin coaxial (200 m)

## Slide 18: Fiber Optic Cable

## Slide 19: Fiber Optic Connectors
single mode fiber
multimode fiber

## Slide 20: Transmission modes
- Full duplex :
devices can send , receive data at the same time (two ways for transmission)
- Half duplex:
one circuit for transmission , so only one device can use the bus (send or receive)
at a time , if two devices sent at the same time collision occurs .

## Slide 21: Layer 1 devices 1- Repeater
A repeater is a network device used to regenerate a signal.
Repeaters regenerate analog or digital signals distorted by transmission loss due to attenuation. Rule : no more than four repeaters can be used between hosts on a LAN.

## Slide 22: 2- Hub
Hubs takes data bits from input port and forward it to all other ports
A Hub is a multi-port Repeater
repeater and hub work in half duplex mode

## Slide 23: Task
1-Types of Network Topologies.
2- Advantages and disadvantages.